## Slide 1
ORACLE CLOUD INFRASTRUCTURE × NVIDIA GR00T
From Synthetic Data
to Real Robot Actions
How OCI + NVIDIA GR00T Cut Training Cost 9.6× Without Sacrificing Quality
Jun Qian · Oracle Cloud Infrastructure
In collaboration with NVIDIA Isaac × GR00T Team
GTC 2027 · San Jose, CA · March 2027
2027
1 / 14

## Slide 2
The Bottleneck Every Robotics Startup Hits
GTC 2027 · OCI × NVIDIA
🏗 DGX or nothing
$200k CapEx before writing a line of robot code
📊 Real robot data at scale
10k labeled demos × $50/demo = $500k data budget
⏱ Slow iteration velocity
3-week hardware procurement vs 5-min OCI spin-up
93%
of robotics startups
never reach
10k labeled demos
Based on seed/Series A
funding analysis 2024–2026
2 / 14

## Slide 3
Our Answer: Full NVIDIA Stack on OCI
GTC 2027 · OCI × NVIDIA
01 GENERATE
Synthetic Data
Genesis 0.4.3 + Isaac Sim 4.5.0
IK-planned trajectories
RTX domain randomization
100 demos in 90 seconds
100% IK success rate
100
demos / 90s
02 TRAIN
GR00T Fine-Tuning
GR00T N1.6-3B (3B params)
2.35 steps/sec on A100
3.07× DDP on 4× A100
$0.0043 per 10k steps
87% GPU utilization
2.35
it/s on A100
03 DEPLOY
Edge Inference
LeRobot v2 → GR00T server
226ms inference latency
Jetson AGX Orin deploy
REST API + 16-step chunks
Policy distillation → 60M params
226ms
inference latency
→
→
Same pipeline we'll demo live today
3 / 14

## Slide 4
Genesis: 100 Demos in 90 Seconds
GTC 2027 · Synthetic Data Generation
SYNTHETIC DATA GENERATION
100% IK success rate — zero failed grasps to filter
38.5 fps simulation on OCI A100-SXM4-80GB
Domain randomization: lighting, color, cube position (±10cm)
Outputs LeRobot v2 format — direct input to GR00T fine-tuning
1000-demo dataset: mixed positions → broader policy generalization
1.1
demos/sec
38.5
fps simulation
100%
IK success
● ● ●
$ python genesis_sdg_planned.py \
--num-demos 100 \
--output /tmp/sdg \
--seed 42
[SDG] Demo 001/100 IK ✓ 0.94s
[SDG] Demo 025/100 IK ✓ 0.91s
[SDG] Demo 050/100 IK ✓ 0.93s
[SDG] Demo 100/100 IK ✓ 0.91s
Total: 100 demos in 92s
100% IK success (0 failures)
Scale to 1000 demos with mixed cube positions for broader policy generalization
4 / 14

## Slide 5
GR00T Fine-Tuning on OCI A100
GTC 2027 · Training Pipeline
FINE-TUNING
Base model: GR00T N1.6-3B (NVIDIA NGC)
Dataset: 1000 demos × 100 steps = 50,000 frames
Hardware: OCI A100-SXM4-80GB (GPU4)
Batch size: 32 · LR: 1e-4 (HPO-optimized)
Training time: 35.4 min for 5000 steps
TRAINING METRICS
Checkpoint | Loss | MAE
Baseline (random) | — | 0.103
500 demos, 5k steps | 0.164 | 0.013 (8.7×↑)
1000 demos, 5k steps | 0.099 (↓39%) | 5%
2.35
it/s · single A100
3.07×
DDP speedup · 4× A100
$0.0043
per 10,000 steps
87%
GPU utilization
5 / 14
closed-loop: 1/20 episodes (5%), avg latency 226ms

## Slide 6
Closed-Loop Eval: Finding the Real Bug
GTC 2027 · Debugging
01
Open-loop MAE: 0.013
Fine-tuned GR00T achieves 8.7× better joint prediction than random baseline. Looks great on paper.
02
Deploy to closed loop → 0% success
Robot never picks up the cube despite excellent MAE. Standard train/eval mismatch?
03
Root cause: CPU vs CUDA backend mismatch
j5 equilibrium: CPU=1.799, CUDA=2.124 (18% difference). Training used CUDA dynamics. PD controller converges to wrong equilibrium at eval.
04
Fix: CUDA backend + 9-DOF + 2 sim steps/action
Align eval environment with training environment. Result: 5% closed-loop success achieved.
↓
Lesson: open-loop MAE is necessary but not sufficient — always validate closed-loop
6 / 14

## Slide 7
DAgger: Closing the Loop with On-Policy Data
GTC 2027 · Online Learning
DATASET AGGREGATION (DAGGER)
The covariate shift problem:
BC trains on expert demos only → policy sees states it was never trained on
Small errors compound: the further from training distribution, the worse it gets
action = β × expert + (1 − β) × policy
iter1: β=0.40 iter2: β=0.28 iter3: β=0.20
Expert interventions per episode decline as policy improves
RESULTS
Iteration | β | CL Success | Interv./ep
BC baseline | 1.00 | 5% | 100 (full expert)
DAgger iter 1 | 0.40 | 52% | 22.8
DAgger iter 2 | 0.28 | 55% | 17.4
DAgger iter 3 | 0.20 | 65% | 10.9
Closed-loop success rate (policy autonomous, no expert blending)
Chart: 
| iter1 | iter2 | iter3
Expert Interventions/ep | 22.8 | 17.4 | 10.9
7 / 14

## Slide 8
Live Demo: The Full 15-Minute Pipeline
GTC 2027 · Live Demo
01
Generate
~90 sec
python genesis_sdg_planned.py
--num-demos 100
100% IK success · 38.5 fps
02
Convert + Train
~14 min
genesis_to_lerobot.py
→ launch_finetune.py
2.35 it/s · loss 0.68→0.16
03
Query Policy
instant
curl localhost:8002/predict
-F image=@frame.jpg
226ms latency · 16-step chunks
04
Evaluate
~3 min
closed_loop_eval.py
--num-episodes 20
Closed-loop success measurement
Total: ~15 minutes end-to-end · ~$0.85 compute cost · Zero hardware required
8 / 14

## Slide 9
Infrastructure Cost: OCI Wins on Every Dimension
GTC 2027 · Cost Analysis
Chart: 
| OCI A100 | DGX On-Prem | Lambda Labs | AWS p4d
$/10k steps | 0.0043 | 0.0045 | 0.018 | 0.041
lower = better
9.6× cheaper than AWS p4d · 4.2× cheaper than Lambda Labs
Provider | $/10k steps | CapEx | Max Burst
OCI A100 | $0.0043 | $0 | 32× A100
DGX On-Prem | ~$0.0045 | $200k+ | Fixed 8×
AWS p4d | $0.041 | $0 | Limited
Lambda Labs | $0.018 | $0 | Limited
FedRAMP / OC2 compliant · US-origin data requirements met
$0 CapEx
FedRAMP
5-min setup
32× A100
9 / 14

## Slide 10
Linear Scaling from 1 to 4 A100s
GTC 2027 · Multi-GPU DDP
75
samples/sec · 1× A100
230
samples/sec · 4× A100 (3.07×)
77% parallel efficiency at 4× (ideal = 4.0×, achieved = 3.07×)
A100
A100
A100
A100
+ torchrun DDP
● ● ●
$ torchrun --nproc_per_node=4 \
launch_finetune.py \
--num-gpus 4 \
--global-batch-size 128
# 230 samples/sec · ~10 min for 5k steps
Chart: 
| 1× A100 (batch=32) | 4× A100 (batch=128)
Throughput | 75 | 230
samples/sec
Burst 1→8→32 A100s on demand
Pay per second · No fixed config
10 / 14

## Slide 11
Measuring the Synthetic-to-Real Visual Gap
GTC 2027 · Sim-to-Real
SIM-TO-REAL ANALYSIS
sim_to_real_gap.py — automated gap scoring
Bhattacharyya Distance
Pixel histogram overlap between SDG and real camera frames. Score 0–10.
FID Proxy
Feature distribution distance via pretrained ResNet. Measures semantic realism.
Policy Confidence Drop
GR00T action certainty on real frames vs synthetic. Quantifies transfer gap.
SDG TUNING LEVERS
Color:
Hue jitter ±15°, brightness ±30%
Lighting:
Ambient intensity, directional angle randomization
Textures:
Material roughness, reflectance variation
Geometry:
Camera FOV, position ±5cm noise
Output:
Gap score 0–10 + actionable Isaac Sim params
Gap analysis guides SDG parameter tuning before deploying to physical robot
11 / 14

## Slide 12
OCI → Jetson: The Deployment Path
GTC 2027 · Edge Deployment
OCI A100
Fine-tune 5k steps
GR00T N1.6-3B (3B params)
~7GB checkpoint
226ms inference
→
Policy Distillation
Teacher → Student
4-layer transformer
~60M params (20× smaller)
BC loss + KL divergence
→
Jetson AGX Orin
Edge deployment
grootserver on Jetson
Target: <100ms
REST API for robot arm
jetson_deploy.sh
policy_distillation.py
groot_franka_server.py
⚠ Distillation pipeline complete on OCI — physical robot validation is 2027 priority
Seeking design-partner with Franka hardware to validate Jetson inference path
12 / 14

## Slide 13
Join the OCI Robotics Compute Program
GTC 2027 · Design Partners
WHAT WE PROVIDE
✓
Free OCI A100 compute for initial fine-tuning runs
✓
Direct pipeline support (Genesis → GR00T → your robot)
✓
Co-authorship on technical publication
✓
Path to GTC 2028 joint talk
✓
Early access to Cosmos world model integration
WHAT WE NEED
→ Manipulation task with proprietary demo data
→ Willingness to share anonymized results
Target Design Partner
Series B robotics startup in NVIDIA ecosystem
Manipulation task (pick, place, assembly, bin picking)
Team that's hit the DGX CapEx wall
US-origin data (FedRAMP / OC2 compliance)
Willing to co-develop and publish results
jun.q.qian@oracle.com
github.com/qianjun22/roboticsai
13 / 14

## Slide 14
ORACLE CLOUD INFRASTRUCTURE × NVIDIA GR00T
The Infrastructure Layer for
Robotics Foundation Models
8.7×
MAE improvement
vs random baseline
$0.0043
cost per
10,000 training steps
15 min
end-to-end pipeline
SDG → train → eval
GR00T N1.6 is the model. OCI is where it learns.
1.
pip install oci-robot-cloud
2.
github.com/qianjun22/roboticsai
3.
jun.q.qian@oracle.com
GTC 2027 · Oracle Cloud Infrastructure × NVIDIA · Session [ID TBD]